## Slide 1: Reducing Pipeline Stalls: Branch Prediction

## Slide 2
Team members
1-Goda Saber Goda
2-Hamed Essam Hamed
3-Mohamed Waheed
4-Mohamed Ahmed
5-Nadia Kamel

## Slide 3: Objective of the Assignment
Understand techniques to reduce pipeline stalls
Implement and evaluate branch prediction
Explore BTB and Return Address Stack enhancements

## Slide 4: Pipeline Baseline Assumptions
5-stage pipeline (IF, ID, EX, MEM, WB)
Perfect I/D cache, result forwarding
Split-phase register access
Branch resolved in EX stage

## Slide 5: Control Hazard Problem
Branches cause 2-cycle penalties if taken
Fall-through path fetches cause wasted cycles
Need to predict and minimize stalls

## Slide 6: Introduction to Branch Prediction
Predict direction in ID stage
Update fetch_pc early if predicted taken
Only mispredicted branches updated in EX stage

## Slide 7: Bimodal Branch Prediction
It predicts whether a branch (like an if statement) will be taken or not taken the next time it's encountered.It uses a single-bit or 2-bit counter for each branch instruction, stored in a Branch History Table (BHT).This predictor is "bimodal" because it considers two outcomes only: taken or not taken — the two "modes."How It Works:The CPU keeps a table indexed by the address of the branch instruction.For each branch, it stores a counter:In a 1-bit predictor: 1 = taken, 0 = not taken.In a 2-bit predictor: more robust to change; needs two wrong predictions to switch direction.When the branch is encountered again, the CPU uses this table to predict the outcome
.Pros:Simple and fast.Effective for branches that behave consistently (e.g., always taken or always not taken).Cons:Poor at predicting loops or alternating branches, since it doesn't account for past behavior beyond the last outcome

## Slide 8: Prediction Penalty Table

## Slide 9: 2 level branch prediction
Level 1:
Branch History TrackingPurpose: Capture the recent behavior pattern of branches
- Components:
Branch History Register (BHR):A shift register that records recent branch outcomes (1 for taken, 0 for not taken)
For local history predictors: Each branch has its own BHR
For global history predictors: All branches share one BHR
- Example: BHR value 1010 means the pattern Taken, Not taken, Taken, Not taken
- Branch History Register Table (BHRT):In local history predictors, this table stores BHRs indexed by branch address
-Size determines how many branches can have unique historie

## Slide 10: 2 level branch prediction
Level 2:
Pattern-Based PredictionPurpose: Use the history patterns to make predictions
Components:
Pattern History Table (PHT): Contains 2-bit saturation counters that make actual predictions
Indexed by the BHR value (or a hash of BHR and branch address)
Each counter has 4 states: 00 (strong not-taken) → 11 (strong taken)Prediction
- Mechanism:
Current BHR selects a PHT entry
The 2-bit counter in that entry makes the prediction
- Example: If BHR=1010 indexes to PHT entry with value 10, predict "taken"

## Slide 11: 2 level branch prediction
Operation Cycle:
Prediction Phase:
Branch address → Index into BHRT (for local history)
Retrieve BHR value
BHR value → Index into PHT
PHT entry provides prediction
Update Phase (after branch resolves):
Update the BHR: Shift in the actual outcome (1 or 0)
Update the PHT counter:
Increment if taken (up to max of 11)
Decrement if not taken (down to min of 00)

## Slide 12: Predictors Implemented
2-bit Saturating Counter: BPred2Bit
Correlating Predictor (2,2): BPred2Level
Compare performance of both

## Slide 13: Branch Target Buffer (BTB)
Cache of target addresses
Used in IF stage
Combined with predictor for faster decision

## Slide 14: BTB Prediction Penalties Table

## Slide 15: Return Address Stack (RAS)
What is the Return Address Stack (RAS)?
The Return Address Stack is a hardware stack that keeps track of return addresses for function calls.
It is a key component in modern CPU pipelines, especially in superscalar and pipelined architectures,
to support accurate return address prediction during speculative execution

## Slide 16: How Does RAS Work?
On a function call:Push the return address (PC of the next instruction) onto the RAS.
On a return:Pop the top of the RAS and predict that as the return address.
This works well because function calls and returns are nested, much like how a stack works.

## Slide 17: Pros and Cons
Pros of RAS
1. High Accuracy for Return PredictionRAS
2. Improved Pipeline
3. Low Latency
Cons of RAS
Limited Depth
Vulnerability to Mismatched Call/Return
Not Effective for Indirect Returns

## Slide 18: Comparison between branching techniques